Case1GW.sim

Beginning in November of 1995, a manufacturing company deposited its radioactive and

nonradioactive by-products onto the ground, contaminating in a 10m x 10m area across, by 15m deep volume.  The deposit is not covered.  The waste represents the only waste unit at the facility.  The site is near the Green Stone River.  The Site was ordered closed by the U.S. Environmental Protection Agency.  Constituents of concern include antimony, strontium 90, and trichloroethylene.  While the site was still active, poor management practices resulted in a considerable amount of wind-blown particulate matter being transported from the site.  Over the years, the residential soil of the nearby town of Fieldview became contaminated.  Residential soil samples have been taken.

Samples have also been taken of the site sediments.  The river is used for drinking water, irrigation, and drinking water for livestock, although it is not used for irrigation of animal feed.  Also, fishing and swimming occur on this stretch of the river.  The local population consumes aquatic life from the river, and locally grown crops and livestock.  There is an intake structure 100ft. downstream from where the contaminants enter the river; this structure is used to supply feed/stock water and irrigation water to two nearby agricultural farms: one in Bend County and one in Blue County.

Contaminants have been measured in the local groundwater system.  Beneath the site, contaminants move through two vadose zones prior to reaching the water table.  Several private and municipal wells use the groundwater from the same aquifer; however, most of the wells are located significantly up gradient from the landfill, are uncontaminated, and do not change the groundwater flow system when pumping.  One pumping well though is located down-gradient of the waste site, and is contaminated with low levels of constituents.  This well is currently being used as a municipal drinking water well for the town of Fieldview.  Besides contaminating the pumping well, the contaminated groundwater also recharges to the Green Stone River.

The area is heavily agricultural and dry deposition of contaminants on plants and consumption by humans is possible.  It is also possible for plants to uptake residual chemicals from the soil.  All records and information pertaining to the site, including maps, photographs, and sampling result summaries are stored at the County Health Department in Fieldview.

In summary, a contaminated soil site has emissions to the air and leaching to the groundwater through two vadose zones prior to reaching the water table.  Contamination reaches a nearby withdrawal well and continues on to contaminate a nearby river.  The same people are exposed to withdrawn groundwater and surface water.  They are also exposed to the contamination from the air pathway and from direct contact with the contaminated surface soils associated with the site.

Case 1

Note: When creating and preparing to run a simulation, it is important to complete the General Info sections for each module in the simulation before attempting to input any of the User Inputs.  This will require two steps, first completing all of the simulations General Info screens beginning with icons in the Global Workspace, and then completing all of the User Inputs for the simulation beginning with the icons in the Local Workspace.

Constituent

General Info

Label: Constituents

Applicable Module: FRAMES Constituent Database Selection

User Input

Select from All Possible Contaminants:

Antimony

STRONTIUM-90

Trichloroethylene

Source

General Info

Label: Source

Applicable Model: MEPAS 5.0 Source in Soil

Options

| Medium type for waste zone - STMEDIA | soil/vadose |  |
| --- | --- | --- |
| Leaching loss route– STINF _ OP | Compute Pathway |  |
| Overland runoff loss route– STOVL _ OP | Turn off pathway |  |
| Suspension loss route– STSUS _ OP | Compute Pathway |  |
| Volatilization loss route– STVOL _ OP | Turn off pathway |  |
| Known Source/Sink – STSRC _ OP | Turn off pathway |  |
| Time interval for simulation – STDELTA _ T | 1 | years |
| Time period for simulation – STMAXTIME | 100 | years |
| Residual mass for simulation - STMINWST | 0.05 | fraction |

Waste Zone

| Thickness of clean overburden- STCLEAN | 0.0 | m |
| --- | --- | --- |
| Thickness– STTHICK | 15.0 | m |
| Length - STLENGTH | 10.0 | m |
| Width - STWIDTH | 10.0 | m |
| Bulk density – STZBULKD | 1.65 | g/cm^3 |
| Total porosity – STTOTPOR | 30 | % |
| Moisture content – STMOISTC | 15.0 | % |
| Volumetric air content – STAIRSPC | 0.15 | fraction |
| Average air temperature - STAVTEMP | 53.006 | F |
| Height above ground of local wind measure - STWINDHT | 10 | m |
| Mean annual wind speed – STAVWINDV | 2.0 | m/s |

Suspension

| Dry bulk density of surface soil - STSBULKD | 1.65 | g/cm^3 |
| --- | --- | --- |
| Fraction of surface cover - STCORRSC | 0%<=x<=1% |  |
| Surface roughness length – STLOCSUR | 1.0 | cm |
| Surface area covered with vegetation - STVEGFR | 0 | fraction |
| Surface area covered with a crust layer – STCRUST | 0 | fraction |
| Number of mechanical disturbances to site | 1 | #/month |
| Maximum wind speed at site – STMAXWIND | 22 | mi./hr. |
| Thornwaite’s Precipitation – Evaporation index - STPEI | 25 |  |
| Aggregate size distribution -- STSDISTB | .33 | mm |
| Is there roadway travel at the site – STROADS | None |  |
| Paved roadway |  |  |
| Distance of roadway traveled – STRTDIST |  | km |
| Average speed of vehicles per trip – STVSPEED |  | km/hr |
| Average weight of vehicles – STVWEIGH |  | Ton |
| Number of round-trips per month – STRTNUM |  | #/day |
| Percent of silt on road surface - STSILT |  | % |
| Average number of vehicle wheels - STWHEELS |  | # |
| Unpaved Roadways |  |  |
| Distance of roadway traveled – STRTDIST |  | Km |
| Average speed of vehicle per trip -- STVSPEED |  |  |
| Average weight of vehicles – STVWEIGH |  |  |
| Average number of vehicles per day -- STRTNUM |  |  |
| Percent of silt on road surface – STSILT |  |  |
| Dry surface moisture content -- STDRYSCO |  |  |

Hydrology

| Elevation of LCD station – STLCDELEV | 223 | m |
| --- | --- | --- |
| Latitude of waste site – STLAT | 47.01 | degrees |
| Elevation of waste site – STELEV | 223 | m |
| SCS curve number - STSCSCN | 39 |  |
| Top soil water capacity – STAVAILW | 1.1 | cm |
| # of days with >0.254mm precipitation – STNUMPRCP | 68 |  |

Monthly Climatology

| Param | Temp | Percip | Windsp | Cloudy | Precip days | Min humid | Max humid |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Unit | F | In | Mi/hr | Fraction | days | % | % |
|  | sttemp | stmprecip | stwindv | stcloud | stmnumpre | strhmin | strhmax |
| January | 30.002 | 1.0 | 0 | 0.79 | 9 | 65 | 82 |
| February | 37.9994 | 1.0 | 0 | 0.76 | 7 | 58 | 80 |
| March | 44.0006 | 1.5 | 0 | 0.68 | 6 | 40 | 70 |
| April | 51.9998 | 1.5 | 0 | 0.64 | 5 | 32 | 70 |
| May | 60.9998 | 1.25 | 0 | 0.59 | 5 | 30 | 70 |
| June | 69.0008 | 1.1 | 0 | 0.53 | 5 | 25 | 70 |
| July | 77.0 | 1.0 | 0 | 0.29 | 2 | 20 | 70 |
| August | 75.0002 | 0.9 | 0 | 0.34 | 3 | 20 | 75 |
| September | 66.0002 | 0.8 | 0 | 0.41 | 3 | 25 | 80 |
| October | 53.0006 | 0.9 | 0 | 0.58 | 5 | 25 | 80 |
| November | 39.9992 | 0.9 | 0 | 0.77 | 8 | 30 | 85 |
| December | 33.0008 | 1.0 | 0 | 0.81 | 10 | 30 | 85 |

Kd’s

| Equilibrium coefficient KD– STKD |  | ML/g |  |
| --- | --- | --- | --- |
| Antimony | 2 | 0.0 | 0 |
|  |  | 0.0 | 100 |
| STRONYIUM-90 | 2 | 2.4 | 0 |
|  |  | 2.4 | 100 |
| Trichloroethylene | 2 | 0.76 | 0 |
|  |  | 0.76 | 100 |
| *YTTRIUM | 2 | 10 | 0 |
|  |  | 10 | 100 |

Constituent Properties

| Water solubility-STSOL |  |  |  |
| --- | --- | --- | --- |
| Antimony |  | 1.0E+06 | mg/L |
| STRONTIUM -90 |  | 1.0E+06 | mg/L |
| Trichloroethylene |  | 1100.0 | mg/L |
| *YTTRIUM -90 |  | 1.0E+06 | mg/L |
| Contaminant inventory quantity-STINVEN |  |  |  |
| Antimony | Worksheet | 1000 | kg |
| STRONTIUM-90 | Worksheet | 1.0 | Ci |
| Trichloroethylene | Worksheet | 1000.0 | g |
| *YTTRIUM-90 | Worksheet | 1E-30 | Ci |
| Decay/degradation half life-STGHALF |  |  |  |
| Antimony |  | 1E+20 | day |
| STRONTIUM -90 |  | 10600.0 | day |
| Trichloroethylene |  | 1E+20 | day |
| *YTTRIUM -90 |  | 2.7 | day |
| Fraction of volatilization release-STVOLRAT |  |  |  |
| Antimony |  | 0.0 | Fraction |
| STRONTIUM-90 |  | 0.0 | Fraction |
| Trichloroethylene |  | 0.0 | Fraction |
| *YTTRIUM-90 |  | 0.0 | Fraction |

Vadose Zone Transport

General Info

Label: Vadose 1

Applicable Model: MEPAS 5.0 Vadose Zone Module

Composition (Soil)

| Soil Class – WP-CLASS | Sand |  |
| --- | --- | --- |
| Percentage of sand – WP-SAND | 92.0 | % |
| Percentage of silt – WP-SILT | 5.0 | % |
| Percentage of clay – WP-CLAY | 3.0 | % |
| Percentage of organic matter – WP-OMC | 0.0 | % |
| Percentage of iron and aluminum – WP-IRON | 0.0 | % |
| Soil type coefficient – WP-SOILCOEF | 4.05 |  |

Characteristics

| pH of the pore water – WP-PH | 7.0 | pH |
| --- | --- | --- |
| Total porosity – WP-TOTPOR | 36.0 | % |
| Field capacity – WP-FIELDC | 9.0 | % |
| Hydraulic conductivity – WP-CONDUC | 570.24 | cm/day |
| Thickness of this layer – WP-THICK | 212.3 | cm |
| Longitudinal dispersivity – WP-LDISP | 0.07 | ft |
| Dry bulk density – WP-BULKD | 1.67 | g/cm^3 |

Constituent Properties

| Adsorption coefficient – WA-SUBKD |
| --- |
| Antimony | 2 | mL/g |
| STRONTIUM-90 | 24.3 | mL/g |
| *YTTRIUM-90 | 10 | mL/g |
| Trichloroethylene | 0.107 | mL/g |
| Water Solubility – WP-SOL |  |  |
| Antimony | 1E + 20 | mg/L |
| STRONTIUM-90 | 1E + 20 | pCi/mL |
| *YTTRIUM-90 | 1E + 20 | pCi/mL |
| Trichloroethylene | 1100 | mg/L |
| Half-life in ground water – WP-GHALF |  |  |
| Antimony | 1E+20 | day |
| STRONTIUM-90 | 10600 | day |
| *YTTRIUM-90 | 2.7 | day |
| Trichloroethylene | 1E+20 | day |

Vadose Zone Transport

General Info

Label: Vadose 2

Applicable Model: MEPAS 5.0 Vadose Zone Module

Composition (Soil)

| Soil Class – WP-CLASS | Sand |  |
| --- | --- | --- |
| Percentage of sand – WP-SAND | 91.2 | % |
| Percentage of silt – WP-SILT | 6.3 | % |
| Percentage of clay – WP-CLAY | 2.5 | % |
| Percentage of organic matter – WP-OMC | 0.0 | % |
| Percentage of iron and aluminum – WP-IRON | 0.0 | % |
| Soil type coefficient – WP-SOILCOEF | 4.0 |  |

Characteristics

| Ph of the pore water – WP-PH | 8.5 | pH |
| --- | --- | --- |
| Total porosity – WP-TOTPOR | 38.0 | % |
| Field capacity – WP-FIELDC | 9.0 | % |
| Hydraulic conductivity – WP-CONDUC | 570.24 | cm/day |
| Thickness of this layer – WP-THICK | 15.2 | Cm |
| Longitudinal dispersivity – WP-LDISP | 0.0 | Cm |
| Dry bulk density – WP-BULKD | 1.64 | g/cm^3 |

Constituent Properties

| Adsorption coefficient – WA-SUBKD |  |  |
| --- | --- | --- |
| Antimony | 2 | mL/g |
| STRONTIUM-90 | 2.4 | mL/g |
| *YTTRIUM-90 | 10 | mL/g |
| Trichloroethylene | 0.1 | mL/g |
| Water Solubility – WP-SOL |  |  |
| Antimony | 1E + 20 | mg/L |
| STRONTIUM-90 | 1E + 20 | pCi/mL |
| *YTTRIUM-90 | 1E + 20 | pCi/mL |
| Trichloroethylene | 1100 | mg/L |
| Half-life in ground water – WP-GHALF |  |  |
| Antimony | 1E + 20 | day |
| STRONTIUM-90 | 10600 | day |
| *YTTRIUM-90 | 2.7 | day |
| Trichloroethylene | 1E + 20 | day |

Aquifer

General Info

Label: Aquifer

Applicable Model: MEPAS 5.0 Aquifer Module

Composition

| Soil Class – WZ-CLASS | Loam |  |
| --- | --- | --- |
| Percentage of sand – WZ-SAND | 65.0 | % |
| Percentage of silt – WZ-SILT | 25.0 | % |
| Percentage of clay – WZ-CLAY | 10.0 | % |
| Percentage of organic matter – WZ-OMC | 0.0 | % |
| Percentage of iron and aluminum – WZ-IRON | 0.0 | % |

Characteristics

| Percentage constituent flux entering aquifer – WZ-FRACT | 100.0 | % |
| --- | --- | --- |
| pH of the pore water – WZ-PH | 7.0 | pH |
| Total porosity – WZ-TOTPOR | 46 | % |
| Effective porosity – WZ-EFFPOR | 20.0 | % |
| Darcy velocity – WZ-PVELOC | 0.017 | ft/day |
| Thickness of aquifer – WZ-THICK | 40.0 | ft |
| Dry bulk density – WZ-BULKD | 1.43 | g/cm^3 |

Concentration Locations

| Usage location Ground water_Well (fcm5) |
| --- |
| Longitudinal distance to well – WZ-DIST | 10000 | cm |
| Perpendicular distance from plume center line to well– WZ-YDIST | 0.0 | cm |
| Vertical distance below water table to well– WZ-AQDEPTH | 20 | cm |
| Longitudinal dispersivity – WZ-LDISP | 1000 | cm |
| Tranverse dispersivity – WZ-TDISP | 330 | cm |
| Vertical dispersivity – WZ-VDISP | 2.5 | cm |

Flux Locations

| Usage location Surface_Water (riv10) |
| --- |
| Longitudinal Distance to flux location– WZ-DIST | 100.0 | m |
| Longitudinal dispersivity – WZ-LDISP | 10.0 | m |
| Tranverse dispersivity – WZ-TDISP | 3.3 | m |
| Vertical dispersivity – WZ-VDISP | 0.025 | m |

Constituent Properties

| Antimony | 0 | mL/g |
| --- | --- | --- |
| STRONTIUM-90 | 2.4 | mL/g |
| *YTTRIUM-90 | 10 | mL/g |
| Trichloroethylene | 0.382 | mL/g |
| Water Solubility – WZ-SOL |  |  |
| Antimony | 1E + 20 | mg/L |
| STRONTIUM-90 | 1E + 20 | pCi/mL |
| *YTTRIUM-90 | 1E + 20 | pCi/mL |
| Trichloroethylene | 1100 | mg/L |
| Half-life in ground water – WZ-GHALF |  |  |
| Antimony | 1E + 20 | day |
| STRONTIUM-90 | 10600 | day |
| *YTTRIUM-90 | 2.7 | day |
| Trichloroethylene | 1E + 20 | day |

Air

General Info

Label: Air

Applicable Model: MEPAS 5.0 Air Module

Climatology

| Reference weather station (AC-LCDREF) | Hanford Met Station |  |
| --- | --- | --- |
| Morning mixing height (AC-MIXAM) | 400.0 | m |
| Afternoon mixing height (AC-MIXPM) | 1400.0 | m |
| Annual precipitation (AC-RAIN) | 6.3 | in. |
| Precipitation days per year (AC-PRENUM) | 68 |  |
| Thunderstorms per year (AC-NUMTS) | 10 |  |

Topographical Data

| Complex Terrain, use wind channel modeling (AR-CHANL) |  |  |
| --- | --- | --- |
| Elevated release, use regional topographical data (AR-TOPTYP) |  |  |
| Elevation of release unit (AR-TOPBAS) |  |  |

Surface Roughness

Regional surface roughness (AR-REGSUR) = all 10 cm

Joint Frequency Data /General

| Data Station (AJ-STATNM) | Hanford Met Station |  |
| --- | --- | --- |
| Anemometer height (AJ-ANEMHT) | 15.2 | m |
| Average roughness length (AJ-RLEN) | 45.5 | cm |
| Wind Speed midpoints (AJ-WINDS) | 0.671 | m/s |
|  | 2.46 | m/s |
|  | 4.48 | m/s |
|  | 6.94 | m/s |
|  | 9.62 | m/s |
|  | 12.53 | m/s |
| Wind joint frequency Calms (AJ-CALMS) A | 0.000 | Number |
| B | 0.000 | Number |
| C | 0.000 | Number |
| D | 0.000 | Number |
| E | 0.000 | Number |
| F | 0.000 | Number |
| G | 0.000 | Number |

Class A

Classes B, C, D, E, F, and G

Surface Water

General Info

Label: Surface Water

Applicable Module: MEPAS 5.0 River Module

| Flow Velocity at contaminant entry point– WW-VELOC | 3 | ft/s |
| --- | --- | --- |
| Depth at contaminant entry point – WW-DEPTH | 10.0 | ft |
| Width at contaminant entry point – WW-WIDTH | 100.0 | ft |
| Usage Location | Ground Water Well (fcm5) |
| Distance from source to location – WW-DIST | 100.0 | ft |
| Average annual discharge at location – WW-DISCHG | 3000 | ft^3/s |

Exposure Pathways

General Info

Label: Groundwater Well

Applicable Model: MEPAS 5.0 Exposure Pathways Module

Scheme: 8

Exposure Controls

| Time to start exposure computation – EC-TEXPOS | 0.0 | Yr. |
| --- | --- | --- |
| Maximum time for reporting – EC-MAXTIM | 100.0 | Yr. |
| Number of time points for evaluation – EC-NTIMES | 50 |  |

# Leach Rates

| Leach rate selection option – EC-LEACHOPTION | User provided leach rate constants |  |
| --- | --- | --- |
| Parent surface soil leach rate constant |  |  |
| Antimony | 1.0 | 1/yr. |
| STRONTIUM-90 | 1.0 | 1/yr |
| Trichloroethylene | 1.0 | 1/yr |
| Progeny surface soil leach rate constant |  |  |
| YTTRIUM-90 | 1.0 | 1/yr. |

Air

| Exposure duration-EA-ATED | 30.0 yr |
| --- | --- |

Pathways:

| Plant Product Ingestion ( Leafy vegetables ( Other vegetables Animal Product Ingestion ( Meat ( Milk | Other Pathways ( Soil-Ingestion ( Soil-Inhalation ( Soil-Dermal ( Soil- External ( Air- External ( Air-Inhalation |
| --- | --- |

Deposition:

| Thickness of soil receiving deposition – EA-TAS | 0.04 | m |
| --- | --- | --- |
| Density of soil receiving deposition – EA-RHOAS | 1.5 | g/cm^3 |

Ground Water

| Exposure duration – EG-DGWED | 30.0 | yr. |
| --- | --- | --- |

Pathways:

| Plant Product Ingestion ( Leafy vegetables ( Other vegetables Animal Product Ingestion ( Meat ( Milk | Other Ingestion ( Drinking water ( Shower water Inhalation ( Air-Volatiles from water ( Shower-Air ( Indoor-Air | Dermal ( Shower |
| --- | --- | --- |

Water Usage:

| ( Animal Drinking |  |  |
| --- | --- | --- |
| ( Irrigation of animal feed |  |  |
| Fraction of the year that surface water is used for irrigation –EG-FIRR | 1.0 |  |
| Irrigation rate - EG-CIRR | 100.0 | L/m^2/m |
| Domestic water distribution time – EG-TWTR | 0.5 | day |
| ( Domestic water is treated – EG-LTRTL |  |  |

Soil

Surface Water

| Exposure duration – EW-DSWED | 30.0 | yr. |
| --- | --- | --- |

Pathways:

| Plant Product Ingestion ( Leafy vegetables ( Other vegetables Animal Product Ingestion ( Meat ( Milk ( Finned Fish ( Shell Fish | Other Ingestion ( Drinking water ( Shower water ( Swimming water ( Shoreline sediment Inhalation ( Air-Volatiles from water ( Shower-Air ( Indoor-Air | Dermal ( Shower ( Swimming ( Shoreline External ( Swimming ( Shoreline ( Boating |
| --- | --- | --- |

Water Usage:

| ( Animal Drinking |  |  |
| --- | --- | --- |
| ( Irrigation of animal feed |  |  |
| Fraction of the year that surface water is used for irrigation –EW-FIRR | 1.0 |  |
| Irrigation rate - EW-CIRR | 100.0 | L/m^2/m |
| Domestic water distribution time – EW-TWTR | 0.5 | day |
| ( Domestic water is treated – EW-LTRTL |  |  |

Recreational:

| Finfish ingestion harvest delay time-EW-TFISH | 10.0 | day |
| --- | --- | --- |
| Shellfish ingestion harvest delay time-EW-TINV | 10.0 | day |
| Thickness of shoreline sediments-EW-TSS | 0.04 | m |
| Density of shoreline sediments-EW-RHOSS | 1.5 | g/cm^3 |
| Finfish fillet correction factor-EW-TISSUE | 1 |  |

Constituent Parameters

| Physical loss half-time in surface soil-EC-SPHALF |  |  |
| --- | --- | --- |
| Antimony | 1E+20 | day |
| STRONTIUM -90 | 10600.0 | day |
| Trichloroethylene | 1E+20 | day |
| *YTTRIUM -90 | 2.7 | day |
| Physical loss half-time in groundwater-EC-GPHALF |  |  |
| Antimony | 1E+20 | day |
| STRONTIUM -90 | 10600.0 | day |
| Trichloroethylene | 1E+20 | day |
| *YTTRIUM -90 | 2.7 | day |
| Physical loss half-time in air-EC-TPHALF |  |  |
| Antimony | 1E+20 | day |
| STRONTIUM -90 | 10600.0 | day |
| Trichloroethylene | 1E+20 | day |
| *YTTRIUM -90 | 2.7 | day |
| Physical loss half-time in surface water-EC-WPHALF |  |  |
| Antimony | 1E+20 | day |
| STRONTIUM -90 | 10600.0 | day |
| Trichloroethylene | 1E+20 | day |
| *YTTRIUM -90 | 2.7 | day |

## Receptor Intakes

General Info

Label Receptor Intake

Applicable Models: MEPAS 5.0 Receptor Intakes Module

| Body weight of individual –IC-BODYWT | 70.0 | kg. |
| --- | --- | --- |
| Exposure duration - IC-EXPDUR | 30 | yr. |
| Water dermal absorption model-IC-DERM |  | EPA Model |
| Ground water ingestion rate – IG-UDWGW | 1.4 | L/d |
| Surface water ingestion rate – IW-UDWSW | 1.4 | L/d |
| Age of receptor at start of exposure – IC-TAGE1 | 0.0 | yr. |
| Age of receptor at end of exposure – IC-TAGE2 | 70.0 | yr. |

### Health Impacts

General Info

Label: Health Impacts

Applicable Model: MEPAS 5.0 Health Impacts Module

# Chemical

Radionuclide

## Credit and Revision History:

Case1GW.GID was originally created for use with FRAMES Version 1.x by Gene Whelan.  This document (Case1GW.SIM) represents the conversion of the Case1GW test case for use in FRAMES Version 2.0 and was last reviewed and verified by Gene Whelan and Richard Leigh on February 3, 2006.